## Slide 1: ELECTRIC CIRCUITS

## Slide 2: I. Circuits
A flow of electrons is called a current.
  Symbol - I
  Unit is Amperes or Amps (A)
  I = q/t
    Current is amount of charge per time.

## Slide 3: B. What is a circuit?
A circuit is any closed loop or conducting path allowing electric charge to flow.
  Closed loop – circuit is ON
  Open loop – circuit is OFF

## Slide 4: II. Electrical Potential Difference
It is the work done moving a charge through an electric field.
Symbol
  V
  V = Won q /q or V=kq/r
  Measured in Volts
  It is the push required to move electrons through a circuit.

## Slide 5: III. Resistance
A property of materials that is a measurement of how much electricity will flow.
  The higher the resistance the less electricity will flow.
  Measured in Ohms ()
  OHM’S Law
    V=IR
    THIS WILL BE LAB #1

## Slide 6: OTHER FORMULAS
P=I2R
P = V2/R
P = IV
This is electrical power measured in Watts. (W)
Don’t forget that P=Work/time as well,
and work is energy (in this case-electrical).

## Slide 7: III. Resistance again
Every substance has a certain amount of resistance.
It depends on:
  LENGTH (L)
  CROSS SECTIONAL AREA (A)
  TYPE OF SUBSTANCE (called resistivity)
    Symbol = 
R =  (L/A)
THIS WILL BE LAB #2

## Slide 8: IV. TYPES OF CIRCUITS
Each circuit has a series of symbols in order to make a schematic.
A schematic is a drawing of a circuit in order to build it.
Symbols:
wire
cell
switch
ammeter
light bulb
resistor
voltmeter

## Slide 9: EXAMPLE CIRCUIT

## Slide 10: SERIES CIRCUIT
Only ONE path for the electricity to flow!
This will be lab #3
#1
#2
#3

## Slide 11: PARALLEL CIRCUIT
Multiple paths for the electricity to flow.
This will e lab #4
#1
#2
#3

## Slide 12: COMBINATION CIRCUITS
Has properties of both series and parallel.
This will be lab #5
#1
#2
#3
#4

## Slide 13
Rules for these circuits will be derived by YOU during the labs you will be doing!